## Slide 1
Prime time
黃宥翔 chris900623@gmail.com
郭昱 ivan010517@gmail.com

## Slide 2
OUTLINE
01
Analysis format
02
Manual

## Slide 3
Analysis format
Power Analysis Flow - Primetime PX

## Slide 4
Analysis format
SAIF (Switching Activity Interchange Format)
  T0 - duration of time found in logic 0 state.
  T1 - duration of time found in logic 1 state.
  TX - duration of time found in unknown “X” state
  TC - sum of the rise (0-to-1) and fall (1-to-0) transitions that are captured during monitoring
  IG - number of 0 - X - 0 and 1 - X - 1 glitches captured during monitoring
  RISE - Rise transitions in a given state.
  FALL - Fall transitions in a given state.
  Toggle Rate (Tr) = TC / duration
  Glitch Rate (Gr) = derate_glitch * IG
    derate_glitch 0.5 (default)
Wave file
  VCD (Value Change Dump)  Prime time
  FSDB(Fast Signal Data Base)  Verdi
Simulation Activity Formats

## Slide 5
Analysis format
Average Power Analysis
Average Power analysis applications
  Packaging selection
The switching activity consists of toggle rates and static probabilities in average power analysis
  Toggle Rate (Tr) for dynamic power
    P(switching) = 0.5 * Cload * vdd2 * Tr
    P(internal) = Energyint * Tr
    power_default_toggle_rate 0.1 (default)
  Static Probability (Sp) for leakage power
    Probability of logic 1 for a node
    P(leak) = (Pleak0 * 1-Sp) + (Pleak1 * Sp)
    power_default_static_probability 0.5 (default)
Default toggle will be applied to the propagation starting point
  primary inputs
  black box outputs

## Slide 6
Analysis format
Time-Based Power Analysis
Peak Power analysis application
  IR drop analysis
Peak power analysis types
  Cycle accurate Peak power analysis
  Event based Peak power analysis

## Slide 7
manual
Primetime manual
Design Compiler
Needed:
PE.v
Dump:
PE_gate.v
PE_syn.sdc
PE_syn.sdf
PE_syn.ddc
Post simulation
Needed:
PE_gate.v
testbenth.v PE_syn.sdf
N16ADFP_StdCell.v
Dump:
PE_wave.vcd
Primetime
Needed:
PE_gate.v
PE_syn.sdc
PE_syn.sdf
PE_wave.vcd
Dump:
Report_power_average_vcd.rpt

## Slide 8
manual
Design Compiler
Please have a look at the Design Compiler.pptx
verilog (gate level netlist)
ddc (save your design)
sdc (Synopsys Design Constraints)
sdf (Standard Delay Format)

## Slide 9
manual
Post-synthesis simulation method 1
Testbenth
Use vcs to dump the file
1. tcsh
2. source post_sim.sh
testbench
Gate Level Netlist
Output Waveform
建議使用絕對路徑
Standard Cell

## Slide 10
manual
Primetime
verilog (gate level netlist)
sdc (Synopsys Design Constraints)
sdf (Standard Delay Format)
vcd(wave file)
Use Primetime
pt_shell -f pt.tcl

## Slide 11
manual
pt.tcl
Your design module name
gate level netlist
Testbench module name/ Your design instance name
*此圖只是對應ppt的操作範例，檔案路徑及名稱請根據自己命名與路徑或作業要求進行修改。

## Slide 12
manual
Power average
(此範例與HW2不同)

## Slide 13
manual
Power average
with clock-gating
(此範例與HW2不同)
Total Power下降

## Slide 14
Thank
you